## Slide 1: NXP LPC11U14F Sample Software for LPCXpresso USB Audio and USB CDC with FFT
11st July 2011
Surya Cahyadi Ph.D.
(Cahyadi.Surya@FotisInc.com)
.
Notes: 1

## Slide 2: Objective
This demo of USB Audio and USB CDC with FFT capability on NXP ARM Cortex-M0 LPC11U family devices.
This demo shows that the hardware resources (ARM core, IRQ handler, USB) on the device can handle complex processing (FFT) and events (Timer IRQ, USB IRQ, etc) efficiently
Possibility of interesting applications using FFT on this devices such as
  Spectrum Analyzer
  Frequency based audio data compression
  High frequency detection

## Slide 3: Block Diagram
Specification
Audio : 10-bit 32k sample/s
FFT Algorithm : 16-bit Fast
Cosine Transform 64 points
VCOM: 115.2 kbps
Three functions on LPC11U14F
Receives the audio data from PC through USB Audio Class
Performs the FFT (transform the audio data to the frequency components
Sends the result to PC via USB CDC (VCOM)

## Slide 4: Data Flow from USB (Audio) to VCOM (FFT)
The audio data (PCM 16-bit) is sent via USB Audio Class @32k sps
FFT operation of 64 samples of audio data available in the buffer is performed every 64 ms
The 64 points FFT result (8-bit data) is sent via USB CDC (Bulk)

## Slide 5: USB Configuration
USB Vendor, Product and Device ID
  USB Vendor ID 0x1FC9
  USB Product ID 0x400F
  USB Device ID 0x0100
USB Audio Class
  Audio Control I/F
  Audio Streaming I/F Alternate Setting 0 – Zero Bandwith
  Audio Streaming I/F Alternate Setting 1 – Operational
    EP 1 ISO
USB Audio Class
  Communication Class I/F
    EP 2 Interrupt
  Data Class I/F
    EP 3 BULK

## Slide 6: FFT Algorithm (Fast Cosine Transform)
N/2-point
FCT
N/2-point
FCT
Discrete Cosine Transform:
Fast Cosine Transform (FCT):
The 64 points Fast Cosine Transform (derivation of DCT) was implemented for FFT
N=64  MULT=192, ADD = 513
Arithmetic Operations were
reduced as much as possible
to minimize processing time

## Slide 7: Processing Time and Workload
FFT Operation and USB Data Transfer in 64 ms frame at system clock 48MHz
Function | Amount (times) | Proc. Time (us) | Total Time (us) | Load
USB Data Transfer | 64 | 10 | 640 | 1.00%
FFT | 1 | 700 | 700 | 1.09%
The processing time shows a very small CPU workload result. There is still many room for more complex application.

## Slide 8: Code Size
The required code size is quite small. There is still many left memory size for more complex application.
Category | Size (byte)
Code | 16,296
Data | 532
Workspace | 2,064
Total Code | 18,892

## Slide 9: Summary
The USB audio & USB CDC sample software with FFT processing has been presented the capability of NXP ARM Cortex-M0 LPC11 family devices .
The small processing time and small memory requirement even with quite complex FFT processing requirement have been shown. More complex algorithm processing implementation on this devices is very possible.
The example of USB composite devices (USB Audio class and CDC class) implementation has been shown.

## Slide 10: Getting Started with Demo (Compile and Flashing)
1. Copy project files LPCXpresso11U14F_usbaudiowithFFT_usbdc &
CMSISv2p00_LPC11xx to your workspace directory.
(CD://USB Audio FFT/LPC11DemoSoftware-LPCXpresso/)
2. Open the project file using LPCXpresso
3. Connect LPCXpresso LPC11U14F Target board J3 to PC’s USB port
4. Compile and flash to board
a. Select the project LPCXpresso11U14_usbaudiowithFFT_usbdc at the Project Explorer
Panel
b. Compile : Project  Build Project
c. Program Flash: Click
d. Select File: LPCXpresso1114_usbaudiowithFFT_usbdc\Debug\
LPCXpresso1114_usbaudiowithFFT_usbdc.axf
e. Click OK
f. Unplug the USB cable

## Slide 11: Getting Started with Demo (Install USB Driver)
1. Connect the USB cable between PC and LPC11U14F Target Board J8
Note: The Target Board SJ1 must be short circuit!
2. The two USB devices will be recognized
a. NXP LPC Vcom device
- Select Install from a list or specific location (Advanced)
- Browse to directory which contain file LPC11xx_vcom.win32
(CD://USB Audio FFT/LPC11DemoSoftware-LPCXpresso/WinXP_Win7-32bit_usb_driver )
- Click Next
b. NXP Speaker will be detected as USB audio class automotically
Check the VCOM number
a. Open Control Panel  System  Hardware  Device Manager
b . Check Port: Example NXP LPC Vcom Device (COM9)  COM9

## Slide 12: Getting Started with Demo (Run FFT Demo)
Run the USB Audio FFT Demo
1. Open the FFT Demo by click following icon.
2. Run the demo by setting the COM # of VCOM and click Start to open the serial communication
Note:
1. Click Stop to stop the communication
2. Click Exit to exit the FFT demo

## Slide 13: Getting Started with Demo (Run Audion Player)
Run the Audio Player and see the demo running
Run the audio player and play music or sound file.
See the spectrum shown in the FFT Demo’s display when the audio plays the music or sound
Example of sound (dir: DemoSound/)
- sweeplin.wav : run the sound from
low to high frequency
- sin500.wav : run sine wave 500 Hz
- sin300_2000.wav: run sine wave 300&2000Hz